## Slide 1: Lotka Volterra with PySyndi
Yash Lal

## Slide 2: Setup
Assumed beta=delta
Swept through 567 parameter sets
  Alpha in [1,9], step=1
  Beta=Delta in [1,1.7], step=0.1
  Gamma in [1,9], step=1
Trained from IC of [5,5]
  Training data was integrating by dt=0.01 from t=0 to 100
  Fit model
Testing from IC of [10,10]
  Training data for validation was integrating by dt=0.01 from t=0 to 100

## Slide 3: Results
Parameter sweep was chosen to avoid extinctions
  Numerical error from the solver pollutes the data
Average testing accuracy: 99.38%
  Some cases had small coefficients on terms that shouldn’t exist (i.e., y^2)
    Nothing too significant
  Accuracy is better when parameters were smaller
One wacky PySyndi breakdown:
  If alpha:beta:delta:gamma was in ratio 1:0.2:0.2:1 i.e., 8:1.6:1.6:8
    “UserWarning: Sparsity parameter is too big (0.1) and eliminated all coefficients”
    I’m not too worried about this happening in the future

## Slide 4: Results
Changing the type of time series
  Time step of the integrator was fixed at 0.01 but training and testing data was taken by selecting every 10th/100th data point
  (Dense): [0,10] with step=0.01: Acc=0.9938
    Even [0,1] with step-0.01 gives Acc=0.9929
  (Wide): [0,100] with step=0.1: Acc=0.6578
Wide data does much worse
  Hypothesis: losing the idea of the “neighborhood” of points

## Slide 5: Testing PySyndi
Yash Lal

## Slide 6: Setup
Use multiple trajectories
  Wider data
  5 trajectories spaced from [0,0] to [50,50]
dt=0.1 in [0,20] for sampling data
Testing on 1 trajectory

## Slide 7: Oscillations
Simple Harmonic Motion and Damped Harmonic Motion
  Success (Acc > 95%, accurate vector field)
  Worked with ranging parameters
    As well as quadratic and (sort of for cubic damping)
      Acc decreases slightly as power of damping term increases
Higher order => harder to learn

## Slide 8: SHM

## Slide 9: DHM

## Slide 10: Exponential Growth and Decay
“UserWarning: Sparsity parameter is too big (0.1) and eliminated all coefficients”
  If decay/growth is too slow, this occurs
    Pops up in random places
Success for small decay/growth rates
  Breaks down with very fast exp decay/growth
  Overfitting occurs and acc declines

## Slide 11: Growth

## Slide 12: Rapid Decay Failure

## Slide 13: Linear and Nonlinear 2D
dx = ax^n+by^n and dy=cx^n+dy^n
For n=1:
  Success in acc >95% (ignoring sparsity errors)
As n increases, hard to find data without numerical instability
  Harder to predict too as before
  Pockets of stability

## Slide 14: 2D Linear

## Slide 15: 2D Cubic Coupled

## Slide 16: From the Paper…
Lorenz Equations
Nonlinear cubic coupled ODEs
Complex fluid flow
Logistic Map

## Slide 17: Thoughts
Data can be finicky and lead to errors if too sparse
More trajectories seem to help
  Compensate for wider data
  Battle between amount of data vs density of data
Higher order terms mess with data
Either seem to get pretty wrong or pretty correct
  Except for cases where overfitting seems to seep away the accuracy

## Slide 18: Cool Plots
Yash Lal